## Slide 1: BLE-based DFU (OTA) Overview
Rapid explanation deck
ESP32 BLE OTA / DFU

## Slide 2: What Was Reviewed
- BLE-based DFU workflow
- ESP32 OTA firmware
- Mobile application as DFU client
- End-to-end flow review (testing pending)

## Slide 3: High-Level DFU Flow
1. Mobile app connects over BLE
2. BLE authentication is performed
3. Firmware sent in small chunks
4. ESP32 writes data to OTA partition
5. Device reboots into new firmware

## Slide 4: BLE Authentication (Security 1 / 2)
- Verifies who is allowed to start OTA
- Prevents unauthorized devices from uploading firmware
- Happens before firmware transfer begins
- Protects BLE transport, not firmware authenticity

## Slide 5: OTA Partitions (Why They Matter)
- ESP32 flash is divided into multiple partitions
- One partition runs current firmware
- Another inactive OTA partition is used for updates
- Running firmware is never overwritten during OTA

## Slide 6: OTA Partition Switching
- New firmware is written to inactive partition
- Current firmware keeps running safely
- After full update, boot partition is switched
- Device reboots only after successful OTA

## Slide 7: Key Takeaway
BLE authentication controls access to OTA,
OTA partitions ensure safe updates.
Firmware authenticity requires Secure Boot or signed OTA.